## Slide 1: High Speed High Power Circuit For Solenoid Control
By: William Poole

## Slide 2: Why is this necessary?
When operating a coil gun there are 2 main faults:
The current damages the devices nearby {heat or arc}
The solenoid remains on to long {induction heater or backfires}

## Slide 3: Overcurrent or Overload
In the event of overcurrent, like a capacitor bank discharging, the devices in the path receive an amount of current above their ratings causing overheating which may cause instantaneous damages.
  Similar to what happens when you tap the leads of a charged capacitor with a screwdriver
Overload is similar, a device is outputting current above the devices rating however this long term current does not damage the device instantly rather over time causing damage to more parts in the system.
  Similar to an air hose in a bottle, slowly expanding till it bursts, destroying the bottle and your ears.

## Slide 4: Timing
When a solenoid operates the B field that wraps around it cause the force generation by the Lorentz force. So, once the objects “center” passes the halfway point the force becomes opposing and the outcome of this becomes an issue.

## Slide 5: Too Long and Way Too Long?
If the solenoid is left on for ~1ms too long past the center point, the solenoid will apply a force to opposite to the velocity slowing the projectile down.
Or, if it is left on way too long past ~1ms the projectile may be dragged back into the solenoid. If the solenoid releases at the worst time it fires backwards. If it doesn’t the worst outcome happens of turning the system into an induction heater.
  This would pour power into the projectile and the solenoid causing both to heat effectively overloading.

## Slide 6: How to prevent this
Slow timing and LONG projectiles
  This is not an ideal solution as longer projectiles will generate more drag and require more energy to reach similar speeds ignoring inefficiency.
  Also, the velocity will likely be reduced
  Technically could determine position as it crosses the middle and disturb the solenoid windings. Also not good
Design a fast circuit
  Technically complicated and harder to install. However, these will make the system theoretically better.

## Slide 7: Design Theory
Solenoid is made of 16awg wire-> 200 wraps -> 5 layers
*16 awg offers the best of size, resistance, and heat stability out of the sizes at around 30amps for 100ms {solenoid excel sheet}
Going off of this the solenoid length is ~2inches long
0.00508in diameter*40=2.032
->choosing projectile length of 3inches to allow 1/2inch distance of detection

## Slide 8: Estimates before entire process
Peak speed: 60m/s
Detection distance desired 1/4inch [6.35mm]{aiming short of sensor spacing}
Total allowed time: 6.35[mm] / 60 [m/s] -> 105uS

## Slide 9: Timing devices
As the projectile is the object which determines the solenoid’s states it cannot maintain a signal to a device.
  Like how a hand does not stay on a light-switch as it turns it on. This a latching circuit, which is to be replicated.
To make a device stay on from a pulsed input there needs to be a latching device. This device takes a signal and with that signal locks or powers itself into a state where it maintains a desired output.

## Slide 10: Timing Design
To detect a solid object such as a coil gun’s ferrous projectile through a barrel an optical sensor was selected.
  Through trial and error the chosen device was a photo-interrupter [LTH-301-32] not a photoelectric switch {to slow 0.5ms}
To interact with this device 2 other devices where used to communicate the pulses:
  An inverting buffer [powers and resets the thyristor]
  A thyristor as a latching device

## Slide 11: Why a thyristor
Cheap at around 66cents
Fast around 20us
simple

## Slide 12: Circuit design
Optical sensor has become a photo interrupter and is shown below

## Slide 13: Function
While circuit is normally on {light is not blocked} there is flow through the photo-transistor
  This means the emitter is at a voltage >0V held there only by the Vbe drop of the bjt/phototransistor ~4v
Once the light is blocked {projectile in position} the circuit becomes an open the emitter voltage drops to 0V at the slew rate or response time of the BJT. [~90% drop is 4V to 400mV is 15us]
This drop then goes to the set and reset paths neccesary

## Slide 14: Photo-transistor Drop time

## Slide 15: Set and Reset
This signal drop goes to buffers which have a response time in the nS range.
Set->1us
Reset emitter drop is at 500uS, reset dropped to 10% original at 515.37u
Likely slew rate for reset signal is the limiting factor

## Slide 16: Set Signal

## Slide 17: Reset Signal

## Slide 18: Reset speed increase

## Slide 19: Drop the reset buffer
If the reset buffer is dropped the signal will propagate at the speed of the emitter resulting in a reset time to the thyristor of 15uS
CONCERN the current through the device may not be enough to latch the thyristor. Review Current Holding of the Device and Current allowed through Photo-Transistor

## Slide 20: Holding Current

## Slide 21: Set and reset now go to the latching device
Set goes to the gate of the thyristor and causes the device to become powered changes PNPN junction to PNNN junction effectively a diode
Reset is a signal that normally supplies the thyristor but once the projectile reaches the optical sensor
This resulting signal is the output
Set time is 2.61u
Reset time is 504.132u [10%]

## Slide 22: Output Waveform

## Slide 23: Output noise
Previous noise signal was done without tying it to a power MOSFET or IGBT. When it is tied however there is a lot of noise.
This was fixed by dropping the resistance with the thyristor giving it more holding current.

## Slide 24: Issue with power mosfet
Vt0 is 3.5V output voltage is 3.48V
Power mosfets will not turn on

## Slide 26: Feedback Issues
There was a spike in the signal in testing that may need fixing could use a high speed comparator to reduce this problem

## Slide 27: Solved and Optimized
Dropped photo interrupter resistance:
  Thyristor latches now
  More current to supply devices
  Power Mosfet Swapped to lower Vt0 model

## Slide 29: Power output [indicates current flow with V drop]

## Slide 30: IGBT Issues
When I got the power-mosfet working
The IGBT also worked but here is a major issue:
  They are power dependent at the input
  A 120A model IGBT has a switching energy of 227µJ (on), 100µJ (off)
  Power output of control circuit estimate peak is ~5v*20mA=0.1watt [J/s]
  227uJ/0.1[J/S]=2.27ms which is too long
  2 paths here, use power MOSFET or high current output device/add higher voltage [use a power MOSFET to turn on an igbt]

## Slide 31: Power MOSFET
A Power-MOSFET at the same current rating of 120A
  Lower voltage rating 100V vs 650V
Has a Vgs of 2.1V making acceptable to use here
Delay time of 81ns and rise time of 168ns -> 249ns

## Slide 32: Power MOSFET to IGBT
Utilizing a cheap power MOSFET and some resistors a solution is approachable
Using a Power MOSFET
  With Vgs<5V ideally <3V
  VDSS >60V {battery concept check or low voltage}
The response time out is still ns but with higher current the energy requirement of a IGBT is solved
  Issue becomes biasing as the voltage is higher but current starts becoming an issue and vgs

## Slide 33: Power MOSFET
Bad idea as VGS is limiting here as if Vg=5v Vgs=2v only have 3v left to operate system
All IGBT VT ~>=5V
CMOS also doesn’t work

## Slide 34: High Voltage amplifier
Using higher voltage through the SCR should allow more energy into the IGBT as well as allowing high current through an SCR
Theoretically do some PMOS shenanigans but probably SCR with resistor is the best